## Slide 1: Welcome at the PLCopen presentation
Notes: Welcome at this presentation
Feel free to adopt this one to your own needs – there is no copyright on it, but make sure you make a reference to PLCopen in your presentation

## Slide 2: PLCopen: changing the world of industrial automation
Eelco van der Wal
Managing Director PLCopen
Notes: Welcome here in the notes of this presentation
These notes provide you additional information on the subject
For certain pictures we use several slides to construct it – making it easier for you to adapt them
For feedback please contact Eelco van der Wal at evdwal@plcopen.org – thanks in advance
Learn and enjoy

## Slide 3: “Agenda”
the activities - introduction PLCopen
the basis - introduction IEC 61131-3
the example - 7 steps to success
Notes: This presentation is split up in 3 sections:
1. the activities of the association PLCopen
2. the basis, providing an introduction into IEC 61131-3
3. The example, structuring via “7 steps to success”

## Slide 4: PLCopen Mission
We want to be the leading association resolving topics related to control programming to support the use of international standards in this field.
Notes: 26
This is the mission
We want to be the leading association resolving topics related to control programming to support the use of international standards in this field.
PLCopen is a vendor and product independent world wide organization.
It focus to users benefits in the pursuit of the IEC 61131-3 standard.

## Slide 5: Programming in its environment
Database Tools
Visualization / HMI
Project design
Tools
Documentation
Tools
Programming
Tools
Debugging Tools
Networking Tools
Configuration
Tools
Simulation Tools
Notes: Programming is just one aspect in solving the whole problem.
Clearly we need to standardize the interfaces between programming and the other environments.

## Slide 6
Organization
TECHNICAL PROMOTIONAL
COMMITTEES
PLCopen
Standardization in Industrial Control programming
Notes: The Board of management, the managing director, and the general meeting provide the guidelines and co-ordinate the strategic goals of PLCopen.
The Technical Committees specify further developments like special application area profiles and compliance levels.
The Promotional Committees, take care of the PLCopen representation, also at fairs and seminars.
Let us look at some of them

## Slide 7: TC1: Standards
IEC 61131-3 is enhanced with Corrigendum & Amendments
Development of joint PLCopen position for IEC
Communication of information from IEC to PLCopen
Improvement proposals
Focused to update, published 2003
Notes: see slide

## Slide 8: TC2: Functions
Definition of Function Block libraries & calling conventions
… for example…
Motion Control Library: the integration of different technologies: logic and motion
Notes: TC 2 – Functions defines Function Blocks libraries.
An example is the activites in Motion Control, merging the Logic and Motion functionality onto one platform

## Slide 9: TC2 – TF Motion Control
Part 1 – FBs released Nov. 2002
Part 2 – Extensions - released June 05
Part 3 – User Guidelines released April 2004 (on-going)
Part 4 – Interpolation – under construction
Part 5 – Homing extensions – V 0.99 for comments
Over 20 companies certified
Check website for full list

## Slide 10: TC3 : Certification …without testing there is no standard…
The IEC 61131 standard only gives basic rules for compliance
Certification gives guidance for users towards real IEC 61131-3 programming systems (e.g. PLCopen certified list shows compliant products)
Notes: 27
Compliancy certification procedures provided by PLCopen assist users with judging the quality and feasibility of programming tools.
It provides a commonly agreed, verifiable basis for module re-usability and for safe investments in further developments.

## Slide 11: TC3: PLCopen Compliance Levels
Application Program
FB
Variable
Code Body
FB
Variable
Code Body
FB
Variable
Code Body
Application Program
FB
Variable
Code Body
FB
Variable
Code Body
FB
Variable
Code Body
Conformity Level &
Reusability Level
Re-usability of Function (Block) libraries
Base Level
Portability of minimal systems
Notes: PLCopen has defined two levels for compliance, aimed at different levels:
Base level as lowest, harmonizing the body code
Conformity Level is the next level, supporting a much wider set of the standard
In addition, Reusability level adds the exchange of Function and Function Blocks between different systems, providing reusability of the core of the programs

## Slide 12: Compliance: Results
Notes: Certified companies are allowed to use these logo’s showing their support to the different levels

## Slide 13: Compliance: Results and Status Base Level (May ‘05)
Accreditation installed: two institutes accredited
Base Level definition ready for IL, ST, FBD, LD and SFC
Base Level Test software ready for IL, ST, FBD and SFC. LD in preparation
Conformity Level and Reusability Level ready for ST – first products certified
26 software packages certified (see website for status)
Notes: see above

## Slide 14: TC4: Communication
Communications interfaces
Interfaces to add-on packages
Application interchange format
Mapping of Profibus has been done
Mapping of CANopen has been done
Notes: Focused to communication at the same level (for instance PLC to PLC) and down to the sensors and actuators via a communication bus.
Rest see above

## Slide 15: TC5: Safety
Support for safe programming techniques
Focus to IEC 61508 “Functional Safety of Safety Related systems”
Guidelines for the use of the IEC standard
Basis for easier commissioning
In combination with the Function Blocks
First results published April 2005
Notes: TC5 Safety was re-initiated in April 2003. The goal is to include safety functionality into the development environment.

## Slide 16: TC6 : XML
Opening up the
development environments
by specifying XML formats for IEC 61131-3
Notes: TC6 has defined an XML schema which acts as an interface between the software tools.

## Slide 17: TC6: XML
Definition of XML schemes for all the IEC languages
Representation of graphical information
Interface to other tools
Basis for distribution of Function Block libraries
Released as V. 1.0 – official release, in June 2005
Consists of a technical doc, the XML schema, and explanation.
Notes: TC6 – XML is a new activity, started in June 2002.
The first results are published in April 2004

## Slide 18: TC6 - XML
Development
tool
Other
Development
tool
Other
Development
tool
Producer of
graphical and
logical
information
Consumer of
graphical and
logical
information
XML
XML
XML
XML

## Slide 19: Coupling XML Schemes
PLCopen Schema
Supplier Schema
Differences
Notes: Comparing a schema of a supplier against the PLCopen schema is easy – with standard XML tools.
With this one easily sees the differences between the implementations, linked to the different areas of use.

## Slide 20: TC6 – XML : status
Official release June 2005
Available on website www.plcopen.org for free dowload
First implementations expected this year
Notes: See above

## Slide 21: PLCopen as a World-wide association
Office in Japan
Main Office in Europe
Office in North America
Office in China
Notes: see above

## Slide 22: General Promotion
PC1: General Promotion
PC3: Promotion North America
PC4: Promotion Japan
PC5: Promotion China
Notes: see above

## Slide 23: PC2: Common training program
The effect of training is often underestimated
Standardization can be very useful and provide a better interface between study and reality
PC2 defined common basics for training..
.. for instance: a IEC 61131-3 training guideline is published
Training facilities fulfilling basic requirements can be certified and listed / referenced to (see website for listing)
Notes: see above

## Slide 24: TC1 : Standards links to IEC 61131-3 Harmonizing the way people look to control
the future is here
Notes: This presentation is not about standards
It is about the way people look to control

## Slide 25: Fiction?
Imagine
* you are in industrial control
* working with 4 different brands of controls
* using different dialects in their programming languages
* struggling to match the level of your software engineers with the operators and maintenance people on the factory floor
* & seeing that your competitor does better
Why? What’s wrong ?
Notes: If the situation above looks like your reality………………

## Slide 26: Out of the jungle
The current variety of problems can be vastly reduced via standardization
... and such a standard is available
Notes: …….. you’d better harmonize the way you all look to control

## Slide 27
IEC 61131-3
“The best thing that happened to industrial control”
Sugar Lantic on Automation Maillist
Notes: … via the IEC 61131-3 standard
First, let us take a closer look into IEC 61131-3.
This published version is ‘just paper’, but it contains a lot of information, so it is better if we focus to the benefits for you.

## Slide 28: The 7 parts of the IEC 61131 Standard
- 1 General overview, definitions IS
- 2 Hardware IS
- 3 Programming Languages IS
- 4 User Guidelines IS
- 5 Messaging Service Specification IS
- 7 Fuzzy Logic IS
- 8 Technical Report
  IS = International Standard
Notes: As you can see it consists of seven parts nowadays.
They are all International Standards
Part 1 provides the general overview
Part 2 deals with the hardware. It does not specify items like CPU, clockspeed or memory.
It deals with the interface to the hardware.
This includes the requirements and test procedures for the hardware, and electrical, mechanical and functional requirements, service, storage and transportation conditions, and test methods and procedures for verification of compliance.
For instance it specifies for a digital input when this input should be seen as logical ‘1’ or logical ‘0’
Part 3 deals with Programming Languages.
These programming languages not only suit Programmable Controllers, but effectively every environment within industrial control and automation. We will get back to this part.
Part 4 deals with user guidelines,
Part 5 with communication to similar systems
Part 7 deals with Fuzzy Logic
And Part 8 is the technical report
(please note – part 6 does not exist. Originally started for communication towards sensors and actuators, it was withdrawn)

## Slide 29: IEC 1131 versus IEC 61131
The good news is – there is no difference
It is an international harmonization of all the IEC standards and the localized versions
Notes: There is much confusion on the re-numbering of the IEC standards.
The change from IEC 1131 to IEC 61131-3 is an international harmonization of all the IEC standards and the localized versions (meaning, the translation into the different languages)
There is no change in the content.

## Slide 30: IEC 61131-3 Programming languages / Industrial Control Programming
Standardizing the way people work with controls
Notes: There are many ways to look at part 3 – the programming languages… but just to make sure we are all talking about the same:
the IEC 61131-3 deals with the interface between
the programmer and the control system
or more direct: what this person sees on his screen

## Slide 31: IEC 61131-3 Programming languages / Industrial Control Programming
...with support for people
with different backgrounds
Notes: or, how these people interface to their control,
no matter which background / color, or level
current environments incorporate them all
Meaning: support for teams with people of different level
or background. So not only programmers, but also installation and maintenance people

## Slide 32: The IEC 61131-3 Standard
Common Elements
Programming Languages
Notes: There are a lot of ways to look to this part 3 of IEC 1131.
The one we use here is very simple: the standard consists of two main blocks:
the Common Elements, valid throughout the specification
and the Programming Languages
Let us take a closer look to the common elements…….

## Slide 33: IEC 61131-3 : Common Elements Variables & Data Types
What is this?
01010101 10101010
Historically
Reference to a physical memory location
Reference to a physical Input
Notes: The first to mention are Datatypes and Variables
Historically, one looked to real memory locations. So what is the example here? 16 bits of digital input? Or output? Or 2 characters, or an integer.
You do not know, and so you can make errors

## Slide 34: IEC 61131-3 : Common Elements Variables & Data types
Temperature_Sensor_1 : Integer
Symbolic representation via labels
Restricted area for I/O mapping
Hardware independent software code
Result: higher transparency & readability
And less errors
Notes: Within IEC 61131-3, one uses variables with sensible names. In addition one tells what we deal with. In this example we use the variable name Temperature_Sensor_1, because that is a clear name, and we couple this to a datatype integer. Now we know we do not get back a string, telling us the temperature in text, but we get a number back.
For the rest of the program we now use the name: this is much more readable and understandable.
Why this datatyping?
Well, IEC 1131-3 is designed to help you to find errors as early as possible in the programming phase.
As you all know, that is the fastest and cheapest way.
Now you know if the data is a string, a date, and integer or 16 bits of Boolean input. There is no confusion about this anymore, and there is
no conflict between different people using the textual representation (that means, the name of the variable)

## Slide 35: IEC 61131-3 : Common Elements
Software Model
Configuration
Resources
Tasks
Notes: Back to the common elements
For this following part , we look at the Software Model as defined in this standard….

## Slide 36: IEC 61131-3 Software Model
Configuration
Communication Function
Notes: At the highest level, the entire system required to solve a particular control problem is called a Configuration.

## Slide 37: IEC 61131-3 Software Model
Configuration
Communication Function
Resource
Resource
Notes: Within a configuration, one or more Resources can be defined.
A resource is like a CPU in your system, providing processor power.

## Slide 38: IEC 61131-3 Software Model
Task
Task
Task
Task
Resource
Resource
Configuration
Communication Function
Notes: A resource include one or more Tasks .
Tasks control the execution of different parts of programs…..

## Slide 39: IEC 61131-3 Software Model
Execution control path
Task
Program
Program
Task
Program
Task
Program
Task
Resource
Resource
Configuration
Communication Function
Notes: Programs can be written in any of the IEC languages….

## Slide 40: IEC 61131-3 Software Model
Global and direct variables
Access path
Execution control path
Variable access path
FB
Task
Program
Program
FB
FB
Task
Program
Task
Program
FB
FB
Task
Resource
Resource
Configuration
Communication Function
Function Block
Variable
Notes: and in the end call function blocks.
Let us compare this to a conventional PLC……….

## Slide 41: IEC 61131-3 vs conventional PLC
Global and direct variables
Access path
Execution control path
Variable access path
FB
Task
Program
Program
FB
FB
Task
Program
Task
Program
FB
FB
Task
Resource
Resource
Configuration
Communication Function
Function Block
Variable
Notes: As shown here in red, a conventional PLC consists of one resource, running one task, controlling one program
As you can easily see, IEC 61131-3 can go well beyond conventional PLCs.
It can provide you with a state-of-the-art multitasking, real-time environment

## Slide 42: Conventional PLC vs IEC 61131-3
Task 1
Program
Task
Resource
Read inputs
Do Calculations
Set Outputs
Endless Loop:
Task 2
Task 3
Task 4
Time based
Events based
Events based
Time based
Notes: The conventional PLC reads the input, does some calculations and sets the output. Then it read again the inputs, does some calculations, and sets again the outputs….and again and again.
It does not matter that there are inputs who do not change during this time.
In IEC 61131-3 tasks, you split up the program in several pieces. And coupled to the needs, you run the tasks on a time basis like every millisecond or minute, or even on event basis: something changes and needs attention.
This task management also makes IEC 61131 applicable to a much broader area as just PLCs. It can be used in a broad range of application area’s, without having to learn additional programming languages.

## Slide 43: Common Elements: Tasks
IEC 61131-3
Embedded
PLCs
PC based
Control
SoftLogic
Drives
LON nodes
DCS
Notes: IEC 61131-3 is used in PLCs, Distributed Control Systems, and even initiated products like SoftLogic / PC-based control.
The same basis is used in all these different environments, making your knowledge and experience usable in all these areas.
Let us look at one in particular…

## Slide 44: Common Elements : Tasks & Datatypes
RPM =2000
Windows CE 3.0
IEC 61131-3 tasks
SCADA & HMI tasks
I/O Communication tasks
OPC
Multi –functional Operator Panel
I/O Communication bus
Notes: … PC based control – here represented as an intelligent operator panel, including Windows CE as operating system. Since this is a multi-tasking operating system, one easily can add tasks like IEC 61131-3 tasks, and combine these with SCADA and HMI tasks and communication tasks, for instance via the OPC standard (OLE for process control)

## Slide 45: IEC 61131-3 : Common Elements
COMMON ELEMENTS
a.o.
Data Types & Variables
Configuration, Resources, Tasks
Programming Organization Units, POUs
  Functions
  Function Blocks
  Programs
Notes: Within the common elements, the Functions, Function Blocks and Programs are called Program Organization Units.
They provide you with reusable code, from macro level to micro level.
Let us have a closer look at them,.
First the functions…...

## Slide 46: Functions …..
* Standard functions
ADD, SQRT, SIN, COS, GT, MIN, MAX, AND, OR, etc.
* Your own defined functions:
FUNCTION SIMPLE_FUN : REAL
VAR_INPUT
A, B : REAL;
C : REAL := 1.0;
END_VAR
SIMPLE_FUN := A*B/C;
END FUNCTION
Notes: We all know functions like Add, Square root, SINus, COSinus, Greater Than, etc.,
IEC has a enormous set of these defined.
You also can create your own functions like this simple_function
Once defined, you can use it over and over again…..
The same is valid for Function Blocks…..

## Slide 47: …. & Function Blocks
Standard Function Blocks
Hysterisis
Q
XIN1
XIN2
EPS
BOOL
REAL
REAL
REAL
Notes: They are like the software equivalent of Integrated Circuits, ICs.
Like black boxes that represent a specialized control function
You have standard defined function blocks, like timers, counters and triggers….

## Slide 48: …. & Function Blocks
Standard Function Blocks
Additional supplied Function Blocks
Hysterisis
Q
XIN1
XIN2
EPS
BOOL
REAL
REAL
REAL
Notes: ..and each supplier can add their own library of blocks, as long as they comply to the defined structure
A particular temperature control loop, or PID, is an excellent example of such a Function Block.

## Slide 49: …. & Function Blocks
Standard Function Blocks
Additional supplied Function Blocks
Your own defined Function Blocks
Hysterisis
Q
XIN1
XIN2
EPS
BOOL
REAL
REAL
REAL
Notes: And you can add your own library of Function Blocks

## Slide 50: …. & Function Blocks
Standard Function Blocks
Additional supplied Function Blocks
Your own defined Function Blocks
All FBs are highly re-usable in same program, different programs or project
Hysterisis
Q
XIN1
XIN2
EPS
BOOL
REAL
REAL
REAL
Notes: No matter which Function Block, they are highly re-usable : in the same program, different programs or even different projects.
You can use them with any of the IEC programming languages, giving you a clear separation between different levels of programmers, or maintenance people.
Their re-usability increases your efficiency, and reduces the number of errors.

## Slide 51: Function Block example
Hysterisis
Q
XIN1
XIN2
EPS
BOOL
REAL
REAL
REAL
1
EPS
EPS
0
XIN2
Q
Notes: Let’s look at an example.
Here shown is a function block in the programming language Function Block Diagram
The FB has the name Hysterisis
It has three inputs, named XIN1, XIN2 and EPS, on the left
They are all of datatype REAL. These names are not very usable, so please in praxis use names that really tell you something….
It has one output (on the right hand side), called Q, of type BOOL
Internally, the FB contains body code…..

## Slide 52: Function Block example
FUNCTION_BLOCK HYSTERISIS
VAR_INPUT
XIN1, XIN2 : REAL;
EPS : REAL; (* Hysterisis band *)
END_VAR
VAR_OUTPUT
Q : BOOL := 0
END_VAR
IF Q THEN
IF XIN1 < (XIN2-EPS) THEN
Q := 0 (* XIN1 decreasing *)
END_IF;
ELSIF XIN1 > (XIN2 + EPS ) THEN
Q := 1; (* XIN1 increasing *)
END_IF;
END_FUNCTION_BLOCK
Hysterisis
Q
XIN1
XIN2
EPS
BOOL
REAL
REAL
REAL
1
EPS
EPS
0
XIN2
Q
Notes: In this example, the body code is written in the language Structured Text
It uses the inputs,does some calculation, and sets the outputs.
The first part deals with the data structure, the second half with the algorithm
In this case it does not use additional data. But it could. No matter which name was used for this local data inside the body, there would be no conflict with its name: one could use this name on different places, without conflict,
This example of data encapsulation takes away a big source of errors.

## Slide 53: Programs : design via building bricks
Automation
application
Start : BOOL;
Emergency : BOOL;
Limit : INT;
PROGRAM
GLOBAL
Local
Type
FUNCTION
INPUT
Local
Type
FUNCTION_BLOCK
INPUT
OUTPUT
IN_OUT
EXTERNAL
Local
Type
Notes: With these Functions and Function Blocks , you can look at a program as a network of these basic building blocks.
In this way complex programs can be broken down into function blocks,
which again can be broken down into smaller function blocks.
This decomposition helps you increasing your efficiency .

## Slide 54: Structure & Advantages of POUs
Create own Function Block Libraries (per application area)
FBs are tested and documented
Make libraries (world wide) accessible
Re-use as much as possible
Change programming to creating networks of FBs
Save 40% on next project
Notes: The strategy to follow with these Program Organization Units is as follows:
You create your own Function Block Libraries (per application area).
These FBs you test and document, for instance in the first project.
After that you make this library accessible to your whole organization.
In this way you improve the re-use of these blocks as much as possible.
With the next program, you are more creating networks of FBs that already exists, giving you the opportunity to focus on the new topics.
In this way one easily can save 40% on this next project. Even figures above 80% are mentioned, but that means that the next project must be quite similar.

## Slide 55: Sequential Function Chart, SFC
Powerful graphical technique for describing the sequential behavior of a control program
Used to partition a control problem
Shows overview, also suitable for rapid diagnostics
Step 1 N FILL
Step 3
Step 2 S Empty
Transition 1
Transition 2
Notes: Sequential Function Chart, or short SFC, is a very powerful graphical technique for describing the sequential behavior of a control program
As such it divides the problem in to smaller units (partitioning of a control problem),
while it provides an excellent overview. This makes it very suitable for rapid diagnostics

## Slide 56: Sequential Function Chart, SFC
Powerful graphical technique for describing the sequential behaviour of a control program
Used to partition a control problem
Shows overview, also suitable for rapid diagnostics
The basic elements are STEPS with ACTION BLOCKS and TRANSITIONS
Support for alternative and parallel sequences
Step 1 N FILL
Step 3
Step 2 S Empty
Transition 1
Transition 2
Notes: The basic elements are STEPS which are connected to ACTION BLOCKS and TRANSITIONS
Only 1 step is active at one time. It runs the coupled action block as long as the transition condition is not true. If this condition becomes true, the previous step (and its action block) is stopped, and the next step (+action block) started. This again till the transition condition becomes true.
SFC supports alternative sequences and parallel sequences, such as commonly required in batch applications.
For instance, one sequence is used for the primary process, and a second for monitoring the overall operating constraints.
And this within the same overview and structure.

## Slide 57: SFC : alternative sequences
Step 1 N FILL
Step 3
Step 2 b S Empty
Transition 1b
Transition 2b
Step 2 a S Empty
Transition 1a
Transition 2a
Notes: Here an example of an alternative sequence: from step 1 it either goes to step 2a or step 2b, depending on which of the transition condition is met. Both conditions need to exclude each other.
As mentioned, parallel sequences are also possible.

## Slide 58: The IEC 61131-3 Standard
Common Elements
Programming Languages
Notes: So much about the common elements. Now to the next group:
the programming languages

## Slide 59: The IEC 61131-3 Programming Languages
Instruction List Structured Text
Function Block Diagram Ladder Diagram
C:= A AND NOT B
A B C
-| |--|/|----------------( )
LD A
ANDN B
ST C
AND
A C
B
Notes: 15
There are 4 programming languages defined – two textual and two graphical.
They all represent the same basic small program here
Regarding the five standardized programming languages no one should be too worried, because all languages except Structured Text have been widely known and utilized for years.
Different regions of the industrial world as well as different fields of applications have contributed to the selection of those languages.
Let us take a closer look at them……..

## Slide 60: The IEC 61131-3 Standard
Common Elements
Programming Languages
Top Down
Bottom Up
Notes: There is more,
and it is directly related to the development systems, which by the way are called PSE’s in IEC, or Program Support Environments.
If we look to the simple picture of the IEC 61131-3 standard, the standard allows two ways to develop your program: bottom up and top down
Whichever you chose, the environment will help you through the whole process
After all, software is here to help us……..

## Slide 61: IEC Programming Environments
Many of them offer:
graphical programming screens
support for multiple windows
mouse operation
pull-down menus
built-in hypertext help function
software verification during design
Notes: and they do..
Many IEC programming systems offer you all you expect from modern environments.
Some of the features are listed here
Compare that to the cryptic character based systems, and you have an additional reason
We showed you the basics of this standard.
To create a better understanding how you can use it, let us look at an example…….

## Slide 62: What are the benefits ?
Notes: Now with all this said – what is the benefit of such a standard…….
Well then we have to look at who is going to use it…?

## Slide 63: Users? Which Users?
Education
Installation
Maintenance
Programming
Process cntrl
Discrete Mnf
System Integrator
YOU ??
Notes: The first problem is: which users?
Where are you, or your company, in this picture?

## Slide 64: Users? Which Users?
Automobile production lines
Water treatment plant
Food processing and packaging machinery
Cable manufacturing
Semi-conductor clean room automation
Theme-park roller coasters
Nuclear waste treatment plant
This wide range encompass different skills
Notes: IEC 61131-3 is used in such a tremendous broad area, that we only can make some general statements about the advantages

## Slide 65: Benefits
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Notes: see above
One has to learn it only once, and can use it on all systems

## Slide 66: Benefits
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Creating a focus to problem solving via software re-usability
(reduced application investment and supplier dependency)
Notes: see above
That creates a focus to the real problem solving part

## Slide 67: Benefits
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Creating a focus to problem solving via software re-usability (reduced application investment and supplier dependency)
Reduced misunderstandings and errors
Notes: because the dialects are gone and the structuring tools are
available, it lead to a better understanding between the
people involved, and to less errors

## Slide 68: Benefits
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Creating a focus to problem solving via software re-usability (reduced application investment and supplier dependency)
Reduced misunderstandings and errors
Programming techniques usable in more environments
(general industrial control)
Notes: IEC 61131-3 is used, and can be used, in a very broad area:
industrial control in general – as shown before

## Slide 69: Benefits
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Creating a focus to problem solving via software re-usability (reduced application investment and supplier dependency)
Reduced misunderstandings and errors
Programming techniques usable in more environments (general industrial control)
Combining harmoniously different components from different
locations, companies or countries, or projects
Notes: and is not restricted to one location or project: for instance
function blocks can be reused over an over again

## Slide 70: Benefits
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Creating a focus to problem solving via software re-usability (reduced application investment and supplier dependency)
Reduced misunderstandings and errors
Programming techniques usable in more environments (general industrial control)
Combining harmoniously different components from different locations, companies or countries, or projects
Increased connectivity (investment protection)
Notes: taking care that your investment is not lost: you are open to the future

## Slide 71: Benefits
Reduced waste of human resources (in training, debugging, maintenance and consultancy)
Creating a focus to problem solving via software re-usability (reduced application investment and supplier dependency)
Reduced misunderstandings and errors
Programming techniques usable in more environments (general industrial control)
Combining harmoniously different components from different locations, companies or countries, or projects
Increased connectivity (investment protection)
Notes: <<no text initially>>

## Slide 72: How to use IEC 61131-3 an example: Structuring Software Development with IEC 61131-3
7 steps to success
Notes: This example will show you the use of the structuring tools in 7 steps.

## Slide 73: Software Development Cycle
Design
/
Development
/
Installation
/
Maintenance..
phases
Notes: We all know about the software development cycle.
Here is one example, but there are more possibilities.

## Slide 74: … software development cycle...
enhancements…..
….. new requirements ...
…. new functionality ….
…. new wishes ...
“… the never ending story of software ”
Notes: Now when you have finalized your project, you will see that there is also another cycle: users want additions, etc. … and so the whole process starts all over again.
This is something that we have to deal with upfront – there will always be changes

## Slide 75: … software quality factors..
Failure Rates: difference between hardware and software
External Quality (‘Perceived value’) versus Internal Quality
Correctness, reliability, robustness, integrity, persistence, safety
ease-of-use
Notes: And still we all expect a good software quality, although the ideas about this quality can differ very much

## Slide 76: What’s the topic here?
Structuring Software Development with IEC 61131-3
meaning: internal Software Quality
In the sense of:
Understandable, Reusable, Verifiable, Maintainable, Isolation
Notes: IEC 61131-3 is focused to the internal software quality, which can be characterized with the following words: Understandable, Reusable, Verifiable, Maintainable, Isolation

## Slide 77: Why Structuring ?
The ever increasing role of Software on system quality: errors cost money
Requirements increased dramatically: 100 lines of codes now 10,000 lines
SW development: not a one-man job anymore, but a team with different know how and background
Commissioning, Installation, Maintenance, and Improvements are essential parts of the development process
Notes: Why Structuring?
Because the requirements on the system have changed, as well as the role of software
Basically, the development process of control software was not in line with the development of hardware.

## Slide 78: Advantages of Structuring
Better Overview
Better Basis for (internal) Communication
Better Focus to problem solving
Basis for reusable software
“Self-documenting”
Notes: Why Structuring?
Because of its benefits.
Benefits like::
- a better overview, not only relevant for the original programmer, but also for commissioning, installation and Maintenance
- a better basis for (internal) Communication
- a focus to problem solving, divided in more than one level
- a basis for the re-usability of the Software
- self dcumenting, because in reality the documentation is often ‘forgotten’ in the process.

## Slide 79: How does that look in IEC 61131-3 ?
7 Steps to Success
with a
Fermentation Control System
Notes: The example will show 7 steps to success

## Slide 80: Fermentation Process
Heater band
Acidic reagent
Alkali reagent
Harvest valve
pH sensor
Temperature
sensor
Feed valve
Agitator
Notes: The whole process is drawn here.
There is a large vessel, which can be filled (Feed Valve)
with the liquid, can be heated with the heater band (cooling
via convection), which can be stirred via the motor,
and where acid and alkali fluid can be added into.

## Slide 81: How to create a control program for this in a structured way?
Notes: Now, how do we create a program to control this process…..

## Slide 82
Step 1 :
Identification of external Interfaces to the System
Feedback from the temperature sensor
Feedback from the pH sensor
Feedback from the valve positions
Feedback from the motor (speed)
Output to the valves
Output to the motor
Output to the heater band
Notes: Step 1 – see slide

## Slide 83
Step 2:
Definition of the main signals between System and Plant
In this example there is no coupling to the plant, but it could have been, like:
… coupling to main vessels with liquids
… coupling to transportation system / filling station after harvesting
Notes: See slide

## Slide 84
Step 3:
Definition of all Operator interactions, overrides and supervisory data
For the operator we define:
…a ‘Start’ button
…a ‘Stop’ button
…a ‘Duration’ input
Now we have defined all the interfaces
Notes: Step 3:
Definition of all Operator interactions, overrides and supervisory data
For the operator we define:
…a ‘Start’ button
…a ‘Stop’ button
…a ‘Duration’ input
And with this we have defined all the external interactions

## Slide 85
Step 4:
Brake down from top in logical partitions
MainSequence - filling, heating, agitating, fermenting, harvesting, cleaning.
ValveControl - operating valves used to fill and empty the vessel's
TemperatureControl - for controlling the temperature
AgitatorControl - agitator motor control
pHControl - PH-control
Notes: In Step 4 we make a brake down from the top in logical partitions (meaning logical functional units)

## Slide 86
Step 5:
Definition of the required POUs (Programs and Function Blocks)
Using the definitions above and
representing it in the graphical way …
Notes: Step 5: Definition of the required POUs (Programs and Function Blocks)
Using the definitions of the previous slide and representing it in the graphical way gives the following diagram…

## Slide 87: Fermentation Control Program
Notes: In this case all basic blocks have been defined, which is one
of the basic steps needed to convert the problem to a solution
(read from left to right side: on the left the inputs, on the right the outputs)
The Function Block Main Sequence is linked to the operator inputs. It is supported by the other blocks for control, which are linked to the relevant inputs and outputs. These additional blocks could be blocks that are delivered by your suppliers, like the temperature control block, using a PID control loop. Alternatively, these blocks can be created by yourself. For instance, this is the case with the block Main Sequence. Looking closer to this block, we could structure its sequence with Sequential Function Charts, SFC, as follows:

## Slide 88: MainSequence in Sequential Function Chart, SFC
Presenting the main
process states
Notes: For the main sequence we would use the structuring tool Sequential Function Chart.
We start at the top with the Initialization: since we do not know the status of the system when we first switch it on, we got to check here the position of the valves, etc.
Then we start filling till the right level has been reached.
Next phase is the heating till the fermentation process starts.
If it starts, we get to the next phase: the actual fermentation process control part.
After completion, we harvest, and after that clean, and we are ready to restart at the top.
This decomposition gives everybody involved a clear overview which sequences are involved, and how it is further decomposed into the function blocks which can be programmed in any of the four languages.
Or, stated differently: our user requirement specification is (nearly) done!

## Slide 89: The Actions Blocks and Transitions can be programmed in any of the four IEC Programming Languages
Notes: Like mentioned before, the action blocks and transition can be programmed in any of the four languages.
For further decomposition, it even can be programmed in SFC, giving another level of structuring.

## Slide 90: The IEC 61131-3 Programming Languages
Instruction List (IL) Structured Text (ST)
Funktion Block Diagram (FBD) Ladder Diagram (LD)
LD A
ANDN B
ST C
C:= A AND NOT B
A B C
-| |--|/|----------------( )
AND
A C
B
Notes: 15
IEC defines four programming languages.
This means that their syntax and semantics has been defined, leaving no room for dialects.
That is what standardization is all about, after all.
There are two Textual and two Graphical Languages.
The textual languages are Instruction List and Structured Text.
The Graphical Languages are Function Block Diagram and Ladder Diagram.
All four languages describe here the same simple program part.
It is just a matter of your background or the problem at hand, which suits you most.
And that is good thing: it gives you a link to your common environment, while offering state of the art programming techniques.

## Slide 91
Step 6:
Definition of scan cycle time requirements for the different parts of the application
In this example we have only one cycle in continuous mode
The remaining time can be used for other cycles like:
…. the filling / transportation system
… checking boundaries and error conditions (in a parallel sequence)
Notes: In this example we have in principle only one cycle, which we can run is a continuous mode. Alternatively, we could have it run on a time basis, for instance every 20 msec. The remaining time can be used for additional sequences, for instance checking or controlling the transportation / bottling system during harvesting, or checking all kind of boundary and/or error conditions.

## Slide 92
And last but not least: Step 7:
Configuration of the System: Definition of Resources, Tasks and linking of programs with physical I/O
Depending on the system involved
Includes physical mapping of symbols to I/O
Mapping of the resource (read: CPU’s in the system)
Definition of the scan cycles and events (as defined in Step 6)
Notes: This phase is dedicated to the system involved. It includes the physical mapping of the symbols to I/O addresses. By using symbolic representation one creates a far better hardware independence. This is especially valid for the creation of the function blocks, which should be hardware independent. By identifying clearly where the physical mapping is done, rewiring in the filed is a lot easier to accomplish. For instance, exchanging the wiring of two digital inputs means that within the physical mapping one has to change two lines. The rest of the program is still valid, and need no changes.
Also here the resources are mapped, meaning which part runs on which processor in the system. IEC 61131-3 support multiprocessing environments, although most of the actual systems still use one processor only for the programs.
Last but not least, one has to map the tasks to the scan cycles and events, as defined in step 6. In this way one can have multiple programs in one system, for instance the fermentation process as described here, supported by overall checks and control of the supporting environments, like bottling or the levels in the supplying chain upfront.

## Slide 93: Conclusion
The Software development process has changed:
  more requirements..
  more functionalities..
  more code..
  more people involved..
  … more requirements / wishes
Structuring and Decomposition are essential parts of modern software development
IEC 61131-3 has the right basis to fulfill your requirements
Notes: The definition of Function Blocks within the IEC 61131-3 programming standard and SFC as structuring tool gives a powerful set of tools for several levels. The use of function blocks at a high level gives an excellent overview on the system under development, resulting in higher readability and transparency. It provides guidance to the modularization of the control problem at hand. In addition it can provide the basis for separating the different development tasks, and focuses attention towards creating re-usable software code at the level of the actual coding.

## Slide 94: The association PLCopen
Together we can make it happen:
Standardization in Industrial Control Programming
WE NEED YOUR SUPPORT FOR THIS !
Join the organization PLCopen
Notes: The association PLCopen is dependent also on its members – we need also your support

## Slide 95: More Information...
www.plcopen.org
Free-of-Charge electronic Newsletter ‘PLCopening’ (in english)
email: evdwal@plcopen.org
Notes: More information?? See above

## Slide 96: Thanks ! End of this presentation