## Slide 1: 21Plus! Training Sept. 7 – 9, 2005 Jeff Brosseau and Bill Sanzo Software Development

## Slide 2: Topics
iBox Utilities (rexterm, resinst, etc.)
GCT
MD Control Tuning
Notes: 1

## Slide 3: Overview
The binary loaded to an iBox contains:
the Resource (which is all the application code written with GCT for the particular iBox);
the Resource Manager (which is the interface software that connects the resource to the operating system along with some utilities);
the Board Support software (which is the software that interfaces to the hardware, e.g. Drivers);
the ROOT software which is the startup code that is called by the firmware when the iBox is loaded.
Notes: 1

## Slide 4: Overview (Cont.)
The Resource Manager includes a user interface (the X-Shell) which supports a list of diagnostic and utility commands.
The X-Shell allows useful commands such as help, dir, copy, etc., as well as an environment for executing utility programs that were created specifically for the resource.
The X-Shell can be interfaced with through the terminal serially (kermit or HyperTerm), or by using the CMS terminal emulator program (rexterm) over the Ethernet from a PC.
Notes: 1

## Slide 5: Overview (Cont.)
One of the most useful utility programs available is resinst.
It allows reading and/or writing any variable in the resource.
The hierarchical variable naming convention used by resinst (and the other utilities) is also used to create entries in the MDB file used for the OPC Server.
This convention is also used in the AIF, RIF, VRF and RLW files loaded to the iBox automatically after startup.
Notes: 1

## Slide 6: iBox Utilities
rexterm
resinst
gfstool
UDP Server
Router
Kermit / HyperTerm
Notes: 1

## Slide 7: rexterm
RexTerm is a terminal emulation program that works over the CMS network using Ethernet to talk to another CMS node.
Since it uses CMS software to connect to an iBox, it cannot display startup messages and some diagnostic messages that are available through the serial port (using a terminal or serial terminal emulation program such as Kermit or HyperTerm).
Notes: 1

## Slide 8: rexterm (cont.)
To start a RexTerm session to an iBox:
Open up a DOS window on the PC.
Set the default drive to F\resource\bin.
Type
rexterm –node 10.1.2.3
Substituting the appropriate node address
If the IP address of the target iBox is not known, switch to the UDP Server task (using <ALT><TAB> or other method). The UDP Server will list the address for each registered node.
Notes: 1

## Slide 9: rexterm (cont.)
To disconnect from rexterm, type #exit.
Be sure to be back at the X-Shell before typing the #exit or you may have problems connecting again later.
If you try to connect to rexterm and the connection fails, you can try typing
rexterm –node 10.1.2.3 –force
The –force parameter will close any previously disconnected sessions that are still active.
Notes: 1

## Slide 10: resinst
resinst is the resource instance data tool.
It is used to read or write variables in the resource.
It can be used with typed commands at the keyboard or with a file containing change commands (like the AIF, RIF, VRF and RLW files loaded at startup).
The resinst commands can be typed from the X-Shell (terminal, terminal emulation program or rexterm).
Notes: 1

## Slide 11: resinst
To use resinst with a file, type the command
resinst –input resource.aif
where resource.aif is a file containing variable change commands.
resinst can also be used for a single command, as in the example
resinst –command Frame1.Scan11.ScanPos1.NoRef:=TRUE
This will execute a single command and return to he X-Shell.
Notes: 1

## Slide 12: resinst
If multiple commands are going to be executed, the edit mode of resinst can be used by typing
resinst –edit
The edit mode allows setting a default path to a function block. Subsequent commands can be relative to the default. A period (.) typed at the end of a function block leaves the default at that level. A period at the beginning of the next command starts at the default. The Greater than symbol (>) is the prompt character.
Notes: 1

## Slide 13: resinst (Sample Session)
(Red characters are user input).
Supervisor>resinst -edit
Warning - TASK "FastTask" still running
The Resource Instance Data Editor, Version 3.1a
(c) Copyright 1992-1998 Eurotherm Gauging Systems, Inc.
>?
[1.0.0] INTERNAL FastTask : TASK EUM ;
[2.0.0] INTERNAL Frame1 : PROGRAM Frame ;
[3.0.0] INTERNAL Globals1 : PROGRAM Globals ;
[4.0.0] INTERNAL BlinkPrg1 : PROGRAM BlinkPrg ;
[5.0.0] INTERNAL BetaSensor1 : PROGRAM BetaSensor ;
[6.0.0] INTERNAL CIOProg1 : PROGRAM CIOProg ;
[7.0.0] INTERNAL CalCont1 : PROGRAM CalCont ;
>BetaSensor1.
BetaSensor1>Frame1.
Frame1>.Scan11.
Frame1.Scan1!>.ScanPos1.
Notes: 1

## Slide 14: resinst (Sample Session)
Frame1.Scan11.ScanPos1>.NoRef
[2.68.34] INTERNAL Frame1.Scan11.ScanPos1.NoRef : BOOL = FALSE ;
Frame1.Scan11.ScanPos1>}
Frame1.Scan11>BetaSensor1.NucData1.NumRdgs
[5.18.31] OUTPUT BetaSensor1.NucData1.NumRdgs : DINT = 257 ;
Frame1.Scan11>BlinkPrg1.
BlinkPrg1>.NeedSetup:=TRUE
[4.0.13] INTERNAL BlinkPrg1.NeedSetup : BOOL = FALSE ;
[4.0.13] INTERNAL BlinkPrg1.NeedSetup : BOOL = TRUE ;
BlinkPrg1>exit
Notes: 1

## Slide 15: gfstool
General File System Tool
User-level file utility
Uses lfstool and rfstool as required internally
Supervisor>exe gfstool
usage: copy|delete|type|dump|concat|compare <src> [<dst>]
[-binary] [-i <InitData>] [-y <Key>] [-quiet]
Supervisor>exe gfstool copy resource.rif ${CFG_CPU}temp.tmp
The GFS Tool, Version 11.0f
(c) Copyright 1992-1998 Eurotherm Gauging Systems, Inc.
Notes: 1

## Slide 16: UDP Server
The UDP Server is responsible for keeping track of the status of all CMS nodes in a networked system.
Any iBox or non-Server PC registers itself with the UDP Server when it starts its’ router.
The UDP Server will keep the other nodes updated on the available nodes so that they can communicate with each other.
There should only be one UDP Server on any CMS network.
Notes: 1

## Slide 17: UDP Server (cont.)
The UDP Server keeps known network names and addresses in a file on the PC (F:\resource\bin\nodes.cms).
This file is updated periodically and is used on the restart of the UDP Server to inform the UDP Server what nodes have been previously registered.
If the nodes.cms file is deleted and the UDP Server restarted, it will not know about any nodes until they are re-registered by restarting an iBox (or restarting the router program on a secondary PC).
Notes: 1

## Slide 18: Router
The Router (cmsrout) functions as the sender and receiver of all CMS messages on a particular node.
All programs that want to send or receive data pass it through the router with an resource name and variable name and the router will figure out how to get to it.
Each node in a CMS network requires a router to be running.
CMS is the Communications Messaging System developed by Eurotherm Controls and used by EGS for most network communications.
Notes: 1

## Slide 19: Graphical Configuration Tool
Based on IEC 61131 Standard for Programmable Controllers
Defined by the International Electrotechnical Commission
Part 3 – Programming Languages
GCT has extensions beyond the scope of IEC 61131-3 (Arrays, Var Refs, etc.)
Notes: 1

## Slide 20: GCT (Cont.)
The languages included in the IEC-61131-3 spec include:
Structured Text (ST)
Function Block Diagrams (FBD)
Sequential Function Charts (SFC)
Ladder Logic
GCT supports ST, FBD & SFC
Notes: 1

## Slide 21: GCT (Cont.)
The Architecture in the IEC-61131-3 spec include:
The Resource (Highest Level in an iBox)
Programs (Highest level Function Blocks)
Function Blocks
Tasks (Used for timing of programs)
Notes: 1

## Slide 22: GCT (Cont.)
The Resource includes:
Tasks, which have an associated Interval or One-Shot to Trigger them
Programs, which are linked to a Task and run when the Task is Triggered.
Notes: 1

## Slide 23: GCT (Cont.)
Programs:
Typically Object-Oriented, i.e. they are specific to an overall function like a scanner, a sensor, an MD Control, etc.
May Contain several layers of Function Blocks
See Examples
Notes: 1

## Slide 24: MD Control
Incremental Proportional / Integral Control
Output from the Function Block is a change (delta) to the Motorized Pot.
All loops are tuned the same (APC too).
Notes: 1

## Slide 25: MD Control
IF Init THEN
PMove := Error * P_Gain ;
IMove := 0.0 ;
ELSIF ShutDown THEN
IF AllowShtDwn THEN
PMove := -1. * Error * P_Gain ; (* If PI goes OFF, remove P-Moves in-transit *)
ELSE
PMove := 0.0 ;
END_IF ;
IMove := 0.0 ;
ELSE
PMove := ( Error - PrevErr ) * P_Gain ;
IMove := Error * I_Gain ;
END_IF ;
Move := ( PMove + IMove ) * ProcGain ;
PrevErr := Error ;
Notes: 1

## Slide 26: MD Control (Cont.)
Tuning Values:
Error Deadband
Error Clamp
Error Protection Clamp
Proportional Gain
Integral Gain
Process Gain
Notes: 1

## Slide 27: MD Control (Cont.)
Process Gain is the Delta Output / Delta Variable
For “Normalized” thickness control, the Process Gain is 1.0 because it is based on % delta speed / % delta thickness. (e.g. a 5% change in linespeed causes a 5% change in thickness)
Proportional Gain is Nominally 1.0, usually set to .8 for safety.
Integral Gain is calculated as P-Gain / the number of loop executions in the response time
Notes: 1

## Slide 28: MD Control (Cont.)
21+ includes an MD Control Diagnostic Display
Allows User entered output
Trends the output (a delta) and the change in the controlled variable (e.g. linespeed)
Allows calculation of Process Gain as well as Response Time and Process Delay
Notes: 1