## Slide 1: 21Plus!
Communications
October 11th 2006
Bill Sanzo

## Slide 2: 21Plus! Plant Layout
Mark-III Scanner
1250mc KR-85 Sensor
Mark-III Scanner
FSIR Transmission Sensor
Remote Network PC
Manager’s Office
MAC II
MAC II
Wonderware HMI
w/Pentium PC
20” Color Touch
Windows XP
Operator Station
Network PLCs
More PCs
Intranet
Remote
Access
Network Switch
Serial PLCs

## Slide 3: Internal Communications
Ethernet Based
OPC Server uses proprietary protocols to extract data from the iBox’s
Wonderware InTouch uses OPC Link as an OPC Client interface to the Server to exchange data
Network File Protocol Server used to transfer files between PC and iBox’s

## Slide 4: External Communications
PLC Links
OPC Server / Client
PC to PC Data Transfer

## Slide 5: PLC Links
Serial or Networked-Based I/O Servers for InTouch
Over 100 I/O Servers Available
PC as Master; PLC as Slave
Don’t Support Arrays

## Slide 6: PLC Link Configuration Tools

## Slide 7: PC to PC Data Transfer
OPC Server Can Provide Data to Network-Based Clients Concurrently with Internal Data Handling
CSV Files Can Be Produced and Transferred Between PC’s
DDE is supported between InTouch and Many other Windows-Based Applications

## Slide 8: OPC Server
DCOM-Based to allow Data Handling Over the Network
All Data From the iBox’s and dBox’s Are Available, Including Arrays
Can Handle Large Number of Data Points
Throughput is Moderate

## Slide 9
Notes: OPC Server – Standard View

## Slide 10
Notes: OPC Server – Frame 1 iBox Data

## Slide 11
Notes: OPC Server – Data Point View

## Slide 12
Notes: OPC Server – Array Data from a Public Group

## Slide 13
Notes: OPC Server - Client View

## Slide 14: CSV Files
Text-Based (Comma Separated Variables)
Standard Format Supported By Most Data Bases, Spreadsheets and Many Windows-Based Applications
All Data From InTouch Is Available, Plus Arrays
Can Handle Large Number of Data Points
Throughput is High, But Not Contemporary

## Slide 15
Notes: CSV File Sample – As Text Only (NotePad)

## Slide 16
Notes: CSV File Example – Using Excel

## Slide 17
Questions?